## Slide 1: GCBASIC
Read Write Modify Solution

## Slide 2: Read-Write-Modify General Rule
On PIC microcontrollers that use GPIO or PORTx registers without a corresponding LATx latch, any bitwise write (e.g., PORTB |= 0x01 or GPIO |= 0x01) performs a Read-Modify-Write cycle.
This means the microcontroller reads the actual pin state, modifies the bits, and writes back—potentially causing unintended changes if pins are inputs or externally influenced.

## Slide 3: Example
Risky examples
  PORTB |= 0x01; // RMW: reads pin state, not internal latch
  GPIO |= 0x02; // Same issue on baseline PICs

## Slide 4: Summary table
Register Type | RMW Risk | Notes
GPIO | ⚠️ High | Common in baseline PICs (e.g., 10F, 12F)
PORTx | ⚠️ High | Mid-range PICs without LATx
LATx | ❌ None | Not present on affected devices

## Slide 5: Is the Read in RMW Internal or ASM-Level?
The read operation in a Read-Modify-Write cycle is internal to the PIC hardware architecture. It’s not something explicitly coded in your assembly instructions — it’s a side effect of how the PIC executes certain instructions at the silicon level.

## Slide 6: What Actually Happens
When you write something like:
  bsf GPIO, 0 ; Set bit 0 of GPIO
The PIC internally performs:
  Read the entire GPIO register (which reflects the current pin states).
  Modify bit 0 to set it.
  Write the result back to GPIO.
This happens even though the instruction itself only says “set bit 0.”
  The microcontroller’s internal logic handles the read and write automatically as part of executing the bsf (bit set f) instruction.

## Slide 7: Instructions That Trigger RMW
Instruction | Description | RMW Risk | Example
BSF f, b | Bit Set f | ✅ High | BSF GPIO, 0
BCF f, b | Bit Clear f | ✅ High | BCF PORTB, 1
INCF f | Increment f | ✅ High | INCF GPIO
DECF f | Decrement f | ✅ High | DECF PORTB
IORWF f, d | Inclusive OR with W | ✅ High | IORWF GPIO, 1
ANDWF f, d | AND W with f | ✅ High | ANDWF PORTB, 1
XORWF f, d | XOR W with f | ✅ High | XORWF GPIO, 1
COMF f, d | Complement f | ✅ High | COMF PORTB, 1
RLF f, d | Rotate Left f | ✅ High | RLF GPIO, 1
RRF f, d | Rotate Right f | ✅ High | RRF PORTB, 1
These instructions read the entire register, modify specific bits, and write back — which can cause unintended effects if the register reflects live pin states.

## Slide 8: Instructions That Avoid RMW
Instruction | Description | RMW Risk | Example
MOVWF f | Move W to f | ❌ None | MOVWF GPIO
CLRF f | Clear f | ❌ None | CLRF PORTB
These instructions do not read the register before writing, so they’re safer for output control:

## Slide 9: New compiler capability
Scans ASM output for unsafe bit-level operations (bcf, bsf, etc.) on volatile ports like GPIO, PORTA, PORTB
Redirects operations to shadow registers (LATx) to isolate logic from hardware state
Tracks pending shadow writes and inserts movwf flushes only when safe and necessary
Handles conditional logic and toggling (e.g., GPIO.1 = !GPIO.1) with multi-step rewrites
Read Write Modify Adapter

## Slide 10: Example Before & After
Original ASM | Rewritten ASM
bcf GPIO,1 | bcf LATA,1 movf LATA,w movwf GPIO
✅ Benefits
Eliminates RMW hazards without manual intervention
Ensures interrupt-safe port manipulation
Produces maintainable, syntactically correct ASM

## Slide 11: Live demo
#option shadowregister GPIO
#option shadowregister PORTA
#option shadowregister PORTB

## Slide 12: GCBASIC
Read Write Modify Solution